Produced by AEA on behalf of South Holland District Council

SOUTH HOLLAND WESTMERE SCHOOL

01 to 30 November 2012

These data are provisional from 01/07/2012 and may be subject to further quality control

| POLLUTANT | NOX | NO | NO2 | O3 | PM10*+ |
| --- | --- | --- | --- | --- | --- |
| Number Very High | - | - | 0 | 0 | 0 |
| Number High | - | - | 0 | 0 | 0 |
| Number Moderate | - | - | 0 | 0 | 0 |
| Number Low | - | - | 719 | 720 | 720 |
| Maximum 15-minute mean | 199 µg m-3 | 94 µg m-3 | 139 µg m-3 | 94 µg m-3 | 90 µg m-3 |
| Maximum hourly mean | 181 µg m-3 | 69 µg m-3 | 134 µg m-3 | 90 µg m-3 | 87 µg m-3 |
| Maximum running 8-hour mean | 158 µg m-3 | 30 µg m-3 | 131 µg m-3 | 86 µg m-3 | 73 µg m-3 |
| Maximum running 24-hour mean | 144 µg m-3 | 17 µg m-3 | 125 µg m-3 | 80 µg m-3 | 43 µg m-3 |
| Maximum daily mean | 144 µg m-3 | 14 µg m-3 | 125 µg m-3 | 80 µg m-3 | 35 µg m-3 |
| Average | 29 µg m-3 | 3 µg m-3 | 25 µg m-3 | 49 µg m-3 | 15 µg m-3 |
| Data capture | 99.9 % | 99.9 % | 99.9 % | 99.9 % | 100.0 % |

+ PM10 as measured by a TEOM with a factor of 1.3 applied to give Indicative Gravimetric Equivalent concentrations.

All gaseous pollutant mass units are at 20'C and 1013mb. Particulate matter concentrations are reported at ambient temperature and pressure.

NOX mass units are NOX as NO2 µg m-3

| Pollutant | Air Quality (England) Regulations 2000 and (Amendment) Regulations 2002 | Exceedences | Days |
| --- | --- | --- | --- |
| Nitrogen Dioxide | Annual mean > 40 µg m-3 | - | - |
| Nitrogen Dioxide | Hourly mean > 200 µg m-3 | 0 | 0 |
| Ozone | Running 8-hour mean > 100 µg m-3 | 0 | 0 |
| PM10 Particulate Matter (Gravimetric) | Daily mean > 50 µg m-3 | 0 | 0 |
| PM10 Particulate Matter (Gravimetric) | Annual mean > 40 µg m-3 | - | - |

Note: For a strict comparison against the objectives there must be a data capture of >90% throughout the calendar year

Produced by AEA on behalf of South Holland District Council

South Holland Westmere School

Hourly Mean Data for 01 to 30 November 2012

Date Created: 18/12/2012