Produced by Ricardo Energy & Environment on behalf of South Holland District Council

SOUTH HOLLAND WESTMERE SCHOOL

01 to 29 February 2016

These data are provisional from 01/10/2015 and may be subject to further quality control

| POLLUTANT | PM10*+ | NO2 | NOX | O3 |
| --- | --- | --- | --- | --- |
| Maximum 15-minute mean | 127 µg m-3 | 491 µg m-3 | 934 µg m-3 | 100 µg m-3 |
| Maximum hourly mean | 105 µg m-3 | 155 µg m-3 | 281 µg m-3 | 100 µg m-3 |
| Maximum running 8-hour mean | 30 µg m-3 | 78 µg m-3 | 104 µg m-3 | 97 µg m-3 |
| Maximum running 24-hour mean | 23 µg m-3 | 69 µg m-3 | 84 µg m-3 | 90 µg m-3 |
| Maximum daily mean | 21 µg m-3 | 69 µg m-3 | 84 µg m-3 | 88 µg m-3 |
| Average | 13 µg m-3 | 22 µg m-3 | 26 µg m-3 | 62 µg m-3 |
| Data capture | 99.7 % | 100.0 % | 100.0 % | 99.9 % |

* PM10 Indicative Gravimetric Equivalent µg m-3

+ PM10 as measured by a TEOM using a gravimetric factor of 1.3 for Indicative Gravimetric Equivalent

All gaseous pollutant mass units are at 20'C and 1013mb. Particulate matter concentrations are reported at ambient temperature and pressure.

NOX mass units are NOX as NO2 µg m-3

| Pollutant | Air Quality (England) Regulations 2000 and (Amendment) Regulations 2002 | Exceedences | Days |
| --- | --- | --- | --- |
| PM10 Particulate Matter (Gravimetric) | Daily mean > 50 µg m-3 | 0 | 0 |
| PM10 Particulate Matter (Gravimetric) | Annual mean > 40 µg m-3 | - | - |
| Nitrogen Dioxide | Annual mean > 40 µg m-3 | - | - |
| Nitrogen Dioxide | Hourly mean > 200 µg m-3 | 0 | 0 |
| Nitrogen Oxides (NO2) | Annual mean > 30 µg m-3 | - | - |
| Ozone | Running 8-hour mean > 100 µg m-3 | 0 | 0 |

Note: For a strict comparison against the objectives there must be a data capture of >90% throughout the calendar year

Produced by Ricardo Energy & Environment on behalf of South Holland District Council

South Holland Westmere School

Hourly Mean Data for 01 to 29 February 2016

Date Created: 11/03/2016

| Michael Davies Ricardo Energy & Environment Gemini Building Fermi Avenue Harwell Didcot Oxfordshire OX11 0QR | Direct Dial: +44 (0)1235 753 234 Reception: +44 (0)1235 753 000 e-mail Michael.A.Davies@ricardo.com |
| --- | --- |